## Slide 1: Epipolar Geometry

## Slide 2: Introduction
When we take an image using pin-hole camera, we loose an important information, ie depth of the image.
Or how far is each point in the image from the camera because it is a 3D-to-2D conversion.
So it is an important question whether we can find the depth information using these cameras.
And the answer is to use more than one camera. Our eyes works in similar way where we use two cameras (two eyes) which is called stereo vision.

## Slide 3
Stereo Camera

## Slide 4: Coplanarity Constraint
Intersection of two corresponding rays
The rays lie in one plane in 3D

## Slide 5: Epipolar Geometry - motivation
Given a point X’ in the plane of the first image
Find the corresponding point X’’ in the second image plane

## Slide 6: Epipolar Geometry
It is used to describe geometric relations in image pairs
Enables efficient search for and prediction of corresponding points
Given a straight-line preserving mapping, the search space reduces from 2D (whole image) t0 1D(line)

## Slide 8: Elements
Epipolar Axis ‘B = (O’ O’’) is the line through the two projection centers
Epipolar Plane Ꜫ = (O’ O’’ X) depends on the projection centers and the point X.
Epipoles e’ = (O’’)’, e’’ = (O’)’’ are the images of the projection centers
Epipolar Lines ‘(X) = (O’’X)’ , ‘’(X) = (O’ X)’’ are the images of the rays (O’’X) and (O’X) in the other image respectively.

## Slide 10: Epipoles and Epipolar Lines
Epipoles e’ = (O’’)’ , e’’ = (O’)’’ are the images of the projection centers
They can also be written as  Ꜫ (image plane)
e’ = (O’O’’)ꓵ Ꜫ’ e’’ = (O’O’’)ꓵ Ꜫ’’
Epipolar lines ‘(X) = (O’’X)’ , ‘’(X) = (O’ X)’’ are the images of the rays (O’’X) and (O’X) in the other image respectively can be written as
‘(X) = Ꜫ ꓵ Ꜫ’ and ‘’(X) = Ꜫ ꓵ Ꜫ’’

## Slide 12: In the Epipolar Plane…
Using a distortion – free lens,
The projection centers O’, O’’
The point X
The epipolar lines ‘(X) , ‘’(X)
The epipoles e’, e’’
The image points X’ , X’’
All lie in the epipolar plane
This simplifies the task of predicting the location of corresponding a point in the other image

## Slide 13: Predicting the location of corresponding points
Task: Predict the location X’’ given X’
The epipolar plane through Ꜫ = (O’O’’X’)
The intersection of the epipolar plane and the second image plane Ꜫ’’ yields the epipolar line ‘’(X)
The corresponding point X’’ lies on the epipolar line “(X)
Reduces the search space from 2D to 1D

## Slide 14: Computing the Key Elements of the Epipolar Geometry
We described the important quantities geometrically, but do not know yet how to obtain them
We will show how to compute them based on the projection matrices and the fundamental matrix.

## Slide 15: Epipolar Axis
The direction of the epipolar axis can directly be computed from the projection centers
b = XO’’ – XO’ (where b Is the homogeneous vector)
This equation expresses that we only know the direction, not the length

## Slide 16: Computing Epipolar Lines
The image points lie on the epipolar lines, X’ ꓰ l’ (X’ is a element of l’)
Same as X’’ = l’’
For X’: X’Tl’ = 0
We can exploit the coplanarity constrain for both points X’, X’’
X’TFX’’ = 0 (substitute l’ = FX’’)
Same for the point X’’
l’’TX’’ = 0
l’’ = FT X’ (this is our prediction (1D space)

## Slide 17: Epipolar Lines Summary
The image points lie on the epipolar lines X’ ꓰ l’ (X’ is a element of l’)
Same as X’’ ꓰ l’’.
For the points X’, X’’, we can exploit the coplanarity constraint
X’TFX’’ = 0
This is valid if
l’ = FX’’ l’’ = FTX’
As then
X’Tl’ = 0 X’’Tl’’ = 0

## Slide 18: Computing the Epipoles
The epipoles are the projections of the projection centers in the other image
Bothe can be computed easily using the projection matrices
e’ = P’XO’’ e’’ = P’’XO’

## Slide 20: Epipoles and Fundamental Matrix
The epipoles are the intersection of all epipolar lines
All l’ : e’Tl’ = 0 All l’’ : e’’Tl’’ = 0
Combining this with the epipolar lines defined through F, i.e., l’ = FX’’ yields for all points X’’
e’TFX’’ = 0
The epipole is the null space of FT

## Slide 22: Epipoles and Fundamental Matrix
Analogus, we obtain for the second epipole x’TFe’’ = 0
Thus,
Null(FT) = e’ null(F) = e’’

## Slide 23: Eigenvectors of F
The epipoles are the left and right eigenvectors of the fundamental matrix.
e’TF = 0 Fe’’ = 0
Thus,
Null(FT) = e’ null(F) = e’’
(They correspond to an eigenvalues of zero)

## Slide 24: Summary
We only assumed a straight-line preserving(uncalibrated)camera.
We discussed the epipolar geometry and key elements such as epipolar lines, axis, plane and epipoles.
Insights: epipolar geometry reduces the search for corrensponences in image pairs from a 2D space to 1D space

## Slide 25: Structure from motion
We have multiple images of the same object from different views.
What you want to get is reconstruct a 3D scene and simultaneously obtain the camera poses of a monocular camera with respect to the given scene. This procedure is known as structure for motion or commonly called as sfm

## Slide 27: Essential Matrix E

## Slide 30
singular value decomposition (SVD)
Degrees of freedom is a combination of how much data you have and how many parameters you need to estimate.